### THE WEST COAST REGIONAL COUNCIL

LOWER WAIHO RATING DISTRICT

ASSET MANAGEMENT PLAN

October 2014

CONTENTS

SECTION I: INTRODUCTION	4

SECTION 2: SERVICE LEVELS	7

SECTION 3: FUNDING	10

SECTION 4: PERFORMANCE MEASURES	11

APPENDIX 1: EXPENDITURE	12

APPENDIX II – INFRASTRUCTURE ASSET REGISTER & INFRASTRUCTURE ASSET MAPS	13

## EXECUTIVE SUMMARY

Under the Local Government  Act 2002 Councils are required to develop ‘Asset Management Plans’ to demonstrate that they are managing the infrastructure for which they have responsibility.

This plan sets out the history of the scheme so there is a record of the major decisions, including expenditure. It identifies the Objective(s) of the scheme as well as the methods of monitoring the condition of the assets, and determining the annual maintenance needed to retain the service level.

The Lower Waiho River Scheme extends from the stopbank below Canavan’s Knob downstream on the left bank for 2.5 kilometres to below the Waiho Loop Terminal Moraine. There are lifestyle blocks, dairy and dry-stock farms as well as community infrastructure such as roads, power and telephone lines that derive benefit from the river control system.

The plan also includes the Infrastructural Asset Register which details all of the Scheme’s assets and their latest valuation.

## SECTION I: INTRODUCTION

1.1 	PURPOSE OF AN ASSET MANAGEMENT PLAN

This Asset Management Plan defines the objective and performance standards of the Lower Waiho Rating District scheme for which the Regional Council has the maintenance responsibility. It also provides a basis upon which the effectiveness of maintenance performance can be measured.

This asset management plan:

- Describes the history of the rating district and identifies it’s assets.

- Describes the methods used to maintain the service level of these assets.

- Complies with the regulatory requirements of the Local Government Act 2002.

# 1.2	BACKGROUND

In 1944 it was proposed to carry out a survey to determine if it was possible to construct a “cut-off” stopbank near Rata Knoll to prevent overflows from the Waiho River flooding Docherty’s Creek. Due to lack of manpower and machinery during the war years this survey was not carried out until 1947 when the Public Works Department received a grant of 50 pounds equivalent to $100 from the Soil Conservation and Rivers Control Council to carry out the work.

In May 1947 the Public Works Department prepared a proposal which included the construction of a stopbank and tree planting to prevent overflows from the Waiho River entering Docherty’s Creek.  This proposal was forwarded to soil Council for approval.

An inspection of the Waiho River by a Soil Council Engineer determined that due to river changes a stopbank and tree planting were no longer required and advised the Westland Catchment Board accordingly.

In November 1948 the Westland Catchment Board received a letter from 6 Lower Waiho farmers regarding possible flooding from the Waiho River and requested urgent action to solve their flooding problem.

The area affected was 1336 hectares and urgent protection works were suggested.

After an inspection of the flooding problems in March 1949 the Westland Catchment Board sought financial assistance from the Crown Lands Department.

On 16th July 1953 Mr C. Milton wrote to the Westland Catchment Board offering financial support for a stopbank.  On 18th November 1953 approval to construct a stopbank with rock protection on the left bank below Rata Knoll was granted by Soil Council.

The stopbank was constructed between April and August 1954.  In June 1956 the bank was raised at the lower end over 370 lineal metres.

On 16/17 December 1965, 100 metres of Milton and Others bank was damaged. This eroded section was to be protected by placing rock riprap along a 140 metre section and to reform the damaged stopbank.   This work was completed on 18 March 1966 by R.E. Clarke Ltd.

On 24 - 25 January 1967 floods damaged the bank over approximately 320 metres.   Large quantities of ice from the Glacier were blamed for the severity of erosion.   Sediment concentration had been very high. The National Park Board considered that the riverbed downstream of the Glacier face rose 21 metres over the last 13 months.   It was considered that very heavy rock should be used over 520 lineal metres. It was also proposed to resite the alignment of the new section along the new river bank. This would give more waterway in flood events. An early estimate of the work was $25,400.

In March 1967 a contract was let to Fergusons Earthmoving Co. Ltd.   A D8 bulldozer was used to divert the river and erect the stopbank.  On 9 March a flood broke through the new bank and removed all the “pushed-up” material. D9 and D8 motor scrapers completed the work. The damage caused required an additional 7,600 m3 of fill and 800 tonnes of rock.  The works were within 8 to 10 hours of completion when on 9 April the deflector bank along with 110 metres of bank across the gut was demolished.  The extra additional cost was $6,840.

The total cost at 30 June 1967 was $16,000. This covered the construction of the stopbank and 10,000 tonnes of rock.

In 1973, 3,000 tonnes of rock was placed on E.J. Gibbs property by H. Langridge and Sons Ltd at a cost of $9,411.

On 18 July 1977, Mr. Millton requested a classification of the area protected by the stopbank to proportion costs for future work.

In September 1978 a design report was produced by the Westland Catchment Board.   The Scheme was designed to provide protection for a 50 year return period flood (estimated at 2,700 cumecs or 17.46 cumecs/sq.km).  Stopbank heights were designed with a freeboard of 1 metre above the design flood level.

In March 1979 the scheme covering from the State Highway bridge downstream to Millton and Others bank was proposed again. Total cost estimates were $120,000.  The Board had prepared a classification to service the Rating District and all settlers had agreed to this both for capital works and future maintenance.

On 12 November 1979 the Soil Conservation and Rivers Control Council approved the Waiho River Scheme at an estimated cost of $155,200.

The classification was adopted by the Westland Catchment Board on 23 October 1979.

On 11-12 March 1982, a major flood inflicted major damage in the Waiho River. Milton and Others stopbank was completely wiped out. Its reconstruction was estimated at $164,000.

The contract was let to Fergusons Earthmoving Co. Ltd and was completed on 24 September 1982 at a total cost of $138,095.50.

The work involved:

- Stopbanks - 68,900 m3 of earthworks

- Bank Protection - 16,072 tonnes of rock.

In March 1984 the Westland Catchment Board resolved to adopt a classification to maintain existing works on the Waiho River.  It was adopted on 16 April 1984.

In 1985 a new stopbank 140 lineal metres in length was built immediately below Canavans Knob. 1,000 tonnes of rock was placed along the outer edge. The bank provided protection for landowners who were affected by flood overflows between Canavans Knob and Rata Knoll.

In March 1986 10 rock spur groynes were placed downstream of the rock faced deflector groyne.  Total rock quantity was 698 tonnes.

Minor works were carried out between 1986 and 1994, on 17 February 1994 an area based classification for the Lower Waiho area was adopted by the Westland Catchment Board.

The total area covered was 1833.4 hectares.

In response to ratepayers’ requests, Council staff prepared a reclassification of the Lower Waiho Rating District in 2003.

A new extended capital – based rating district was ratified in the Council’s Annual Plan adopted on August 2003.

Due to a sudden shift in the main Waiho River channel, the Rubbish Dump stopbank was extended upstream over a distance of 400 metres to “tie into” the downstream side of Canavan’s Knob in November 2005.

1.3	DESCRIPTION OF ASSETS

The Rating District assets consist of all those works outlined in the Infrastructural Asset Register. The total replacement value of these works was $4,070,895 as at June 2014.

The capital value of land and buildings within the confines of the scheme is $4M.

1.4	MAINTENANCE EXPENDITURE

Appendix I shows expenditure since 1994. The average annual expenditure is $40,791.

## SECTION 2: SERVICE LEVELS

2.1	OBJECTIVE

The objective of the Rating District is To reduce bank erosion and flooding between Canavan’s Knob and the Waiho Loop Terminal Moraine on the left bank.

Cross-section and flood flow analysis indicates that the current service potential of the whole of the Rubbish Dump stopbank and 20% of the Milton & Others stopbank is capable of containing less than 2,050 cumecs, which is the current estimate of the 1 in 50 year return period flood with 900mm freeboard.

The rating district has accepted there is a need to increase the level of protection afforded by the stopbank and are considering raising its height to be able to contain at least 2,050 cumecs plus freeboard.

2.2	MAINTENANCE PROGRAMME

An annual maintenance programme will be prepared each year in consultation with the Lower Waiho ratepayer committee prior to adoption by the Council for inclusion in the Annual Plan.

In preparing the annual maintenance programme consideration will be given to:

- works requiring immediate repair.

- works anticipated as being required given a ‘normal’ season.

- flexibility to meet unbudgeted damages.

An annual report will be presented to the Rating District outlining the condition of the scheme assets and maintenance works and expenditure required for the coming financial year.

2.3	MAINTENANCE ISSUES

Stopbanks

Stopbanks are man made structures generally running parallel to the flow of the river that are built to raise the bank level and hence increase the capacity of the river. They are usually constructed of compacted river gravels with a grass cover and do not have the strength to resist the erosive forces of a river in flood without adequate bank protection works in place.

Maintenance includes repair of any scouring, vegetation removal to facilitate access, control of stock to prevent damage to stopbank batter slopes, topping up of stopbanks as required to maintain stopbank capacity in terms of design.

Stopbanks can potentially be damaged by:

- Failure of a training groyne such as a rock retard which can allow the full force of the river to suddenly run along a relatively unprotected stopbank, and cause scouring of stopbanks in excess of 50 metres in length

- Overtopping: Stopbanks are generally not designed to sustain overtopping. They may however be capable of sustaining minor overtopping for a short duration in flows not exceeding 100mm in depth over the top of the bank. Overtopping of durations greater than an hour may scour the back batter resulting in failure of the structure, it is therefore important to ensure there is an even and strong vegetation cover on the landward batter.

- Piping: Flow through porous bank or foundation material can wash out fines leading to a collapse.

- Stock and Vehicles: Can remove cover and wear ruts in surface resulting in weakness.

- Construction: Construction of pipelines cables under stopbanks as well as holes on top of stopbanks can weaken the structure. Drainage channels should not be located at the toe of stopbanks.

- Earthquake: Stopbanks can be damaged in the event of an earthquake by cracking vertical or horizontal displacement, or by liquefaction of the foundation material.

Erosion Control Works

Erosion control works consist of rock placed in continuous riprap, spur groynes, stub groynes, strongheads, hook groynes, and in river training retards. 	Erosion control and river training structures are built to provide protection to stopbanks and natural bush from the rivers erosive forces during floods by training the river into a stable pattern or reduce velocities along stopbanks using stub rock groynes.

Only limited river training is carried out by way of channel improvements by diversion or extraction of river gravels. This is generally accepted as only having a limited and temporary influence on the channel hydraulics (performance).

Erosion control structures are constructed to absorb the energy of the river, to control the alignment of the flow of the rivers, and subsequently give the required protection to stopbanks and natural banks. Because of this they are the areas with the major exposure to damage. 	The meander of a river can change significantly by floods of only moderate duration.  This can result in an acute angle of attack of protection structures resulting in damage which is disproportional to the flood discharge. Likewise erosion control works already weakened from previous floods may sustain damage disproportionate to the flood discharge.

It is very important to ensure damage to bank protection structures is undertaken swiftly and to ensure:

- Rock training walls are kept to the required height to lessen failure.

- Any slumping of rock off strongpoints, spur groynes and rip rap are topped up.

- Rock is of a durable nature, angular and of the correct grading size.

2.4	DAMAGE EXPOSURE

River control works are constructed in a very high energy environment with the purpose of resisting and absorbing some of that energy.  It is considered that no matter what the standard of maintenance carried, it is inevitable that damage will occur to structures.

An assessment of maximum damage potential was derived from estimating the damage ratios and costs for three flood events and is in vicinity of $360,000.

| FLOOD EVENT SIZE | VALUE | DAMAGE RATIO | DAMAGE EXPOSURE |
| --- | --- | --- | --- |
| 20 Year | $1,944,854 | 10% | $194,485 |
| 100 Year | $1,944,854 | 20% | $388,970 |
| 500 Year | $1,944,854 | 20% | $388,970 |

## SECTION 3: FUNDING

3.1	Maintenance

Maintenance is funded by targeted rates, the level of rating being determined each year in the Annual Plan process following:

- Preparation of an annual works programme and corresponding budget.

- Consultation with Rating District.

- Adoption of draft programme and budget by Council.

- Adoption of final Annual Plan by Council.

3.2	Damage Repairs

Routine damage repairs are funded by a combination of:

- carrying out work as scheduled in annual works programme.

- reprioritising works identified in the annual works programme.

- use of financial reserves.

Major damage repairs would be funded by loans raised by the Council and repaid by targeted rating over a number of years.

3.3	Financial Reserves

Financial reserves are held within each rating districts account to provide the following.

- meet the costs of unscheduled works.

- enable an immediate response to flood damage repairs.

- prevent major fluctuation in rating levels annually.

The level of financial reserves held in each rating account is determined by the assessment of risk damage and the need for unprogrammed works.

3.4	Depreciation

Rating District schemes are designed to be maintained in perpetuity by constantly repairing and replacing component parts which are damaged by the constant wear and tear. Because there is a constant cycle of replacement of elements of the infrastructure, depreciation of the value of the assets is not appropriate and funding of depreciation is not necessary. This approach is consistent with the NZ Infrastructure Asset Valuation and Depreciation Guidelines (Ref  Version 1.0 Section 5.4.4)

## SECTION 4: PERFORMANCE MEASURES

The overall performance measure is that the infrastructure assets are maintained to meet their service levels at all times.

The following procedures will be adopted to ensure the adequacy of maintenance.

Annually

- Produce annual works report for the rating district to include type of work to be undertaken, quantities, location and costs.

- Organise contracts for agreed scheme work, oversee contract completion and report to Council.

(iii)	Report on works undertaken during the previous financial period to the rating district ratepayers and Council.

Performance Measure

No reports of stopbanks or erosion protection works requiring repairs without an agreed programme of remedial work in progress.

Triennially

(i)	Re-fly aerial photographs of the area, analysing these photographs to assess changes in river meander patterns that could impact on Rating District Assets.

(ii)	Re-measure cross section river profiles to determine whether the riverbed is stable, or aggrading, and to identify management issues or options.

(iii)	Revaluation of the asset schedule to include any additional rock placed on stopbanks and bank protection works over the three year period.

(iv)	Review this Asset Management Plan

Performance Measure

Report to Council and ratepayers on revaluation of assets and the Plan review.

## APPENDIX 1: EXPENDITURE

Works expenditure from 1994

| 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1,332 | 935 | 8,428 | 20,276 | 1,873 | 1,586 | 44,909 | 3,856 |
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 |
| 19,568 | 1,879 | 865 | 126,874 | 4,499 | 697 | 151,592 | 63,234 |
| 2010 | 2011 | 2012 | 2013 | 2014 |  |  |  |
| 87,133 | 3,018 | 23,637 | 29,073 | 261,347 |  |  |  |

| Total Expenditure | $ 856,611 |
| --- | --- |
| Average Expenditure | $ 40,791 |
| Average Expenditure as a % of Asset Value | 2.09% |

As at 30 June 2014, the value of the Lower Waiho Rating District Scheme assets was $1,944,854

## APPENDIX II – INFRASTRUCTURE ASSET REGISTER & INFRASTRUCTURE ASSET MAPS

| LOWER WAIHO RATING DISTRICT |  |  |  |
| --- | --- | --- | --- |
| Infrastructural Assets - Amended to 30 June 2014 |  |  |  |
| Refer to Drawing no 888/50 Sheet 1 |  |  |  |
|  |  | Fill | Rock | Stockpile |
|  |  | m³ | tonne | tonne |
| 1 | Rubbish Dump Stopbank over 836m | 23008.75 | 964 |  |
|  | Height 3 metres, 4 metres topwidth |  |  |  |
|  | 2:1 batters |  |  |  |
| 2 | Rubbish Dump Stopbank facing over 836m |  | 12324 |  |
| 3 | Deflector Groyne at lower end of Rubbish Dump bank |  | 3605 |  |
| 4 | New Rubbish Dump to Rata Knoll extension over 1020m |  |  |  |
| 5 | Milton & Others Stopbank over 1,180m | 50,600 |  |  |
| 6 | Riprap over 1180m |  | 18755 |  |
| 7 | New rock spur |  |  |  |
| 8 | Rock Stockpile |  |  | 600 |
| 9 | Stockpile (Canavans Knob) |  |  | 300 |
| 10 | Rock Deflector (Canavans Knob) |  | 1240 |  |
|  | Summary | 73608.75 | 36888 | 900 |
|  | Unit Rates | $ 7.50 | $ 32.00 | $ 1.00 |
|  | Calculated Costs | $ 552,065.63 | $1,180,416.00 | $ 900.00 |
|  | Total Estimated Assets as at 30 June 2014 | $ 1,733,381.63 |  |  |
|  | Add 10% Contingencies to cover Design etc | 173,338.16 |  |  |
|  | Add 2% for Resource Consent Costs | 38,134.40 |  |  |
|  | Total Including Contingencies | $ 1,944,854.18 |  |  |